## Slide 1: Remote Controlled R2-D2 Sith Happens
Daniel Suen
Steven Paek

## Slide 2: Project Summary
Remote Controlled “R2-D2” using RC Car Frame and Controller
R2-D2: Movement controlled by joystick, plays audio based on controller inputs, fires nerf bullets, and uses RGB LEDs to display temperatures
Controller: Uses joystick to control movement, buttons for sound selection and other functions, (goal) text-to-speech keyboard, and all communication via XBee

## Slide 3: Project Objectives
Digital Objectives: Xbee UART Communication, PWM Control for Motors, Microprocessor Controls for R2-D2 and Controller (GPIO), and Nerf Bullet Control
Analog Objectives: Battery Recharge Circuit, Joystick Control, Thermistor-LED Control, and Audio Output from Speaker

## Slide 4: Technology Selection
MSP432P401R: Up to 48MHz CPU, FPU, 14-bit ADC, UART, 16-bit Timers with PWM (Robot/Controller)
Xbee: RF Module IEEE 802.15.4 Standard, UART Communication (Robot/Controller)
L293D: PWM Motor Driver (Robot)
LTC1661: 10-bit External DAC, 2.7V to 5.5V Supply (Robot)
LM386: Low Voltage Audio Power Amplifier (Robot)
Joystick: Analog Joystick

## Slide 5: Flowchart/Diagrams

## Slide 6: Task Assignment
Printed Circuit Boards (PCBs)
  R2-D2 PCB (Steven)
  Controller PCB (Daniel)
  Battery Recharge PCB (Daniel)
R2-D2 (Robot)
  Motor PWM (Steven)
  Audio Circuit with External DAC (Steven)
  Thermistor-LED (Steven)
  Other I/O - Nerf Gun, etc. (Steven)
Controller
  Joystick Control (Daniel)
  Controller I/O for Sound, Nerf Gun, and Movement (Daniel)
  XBee Communication (Daniel)

## Slide 7: Gantt Chart